## Slide 1: CPE 301 Publish Compass
Martin Jaime
Email: jaimem5@unlv.nevada.edu

## Slide 2: AIM & ACCOMPLISHMENT
AIM:
Read HMC5883L with Atmega328P over I2C.
Communicate with another the ESP8266 over UART.
Publish data to ThingSpeak.com with ESP8266.
ACCOMPLISHMENT
IoT device that publishes data to the cloud.
IMPLEMENTATION
Robotics
Mobile devices

## Slide 3: SCHEMATICS

## Slide 4: DESIGN STAGES
Main Components
AVR ATMEGA328p
HMC5883L
ESP8266
Interfaces
Atmega328p – HMC5883L using I2C – Address (0x3C)
Atmega328p – ESP8266 using USART
IoT : Thingspeak.com server

## Slide 5: CODE DEVELOPMENT
Initialization
  Amega328P initializes its UART and I2C ports
  Initialize HMC5882L for continuous acquisition at 15Hz
  Initialize ESP8266 with initialization script init.lua
Data Collection
  Collect magnetic field magnitudes in gauss units on three axis of the sensor.
  Calculate angle of sum of vectors parallel to breadboard.
  ESP8266 publishes prepared data.

## Slide 6: OIT/Visualization

## Slide 7: DEMO SNAPSHOT/VIDEO